4x 1.5” segment displays
Common Annode (High)

ESP32-S2 as the controller.
Each diode can safely pull up to 30mA at 2v it appears.
So we’ll use a 1.8v reg and perform calculations assuming 30mA per channel.

7*4*30 = 840mA. We’ll use a 1.8v LDO Rated at 1A, which should be sufficient.
The output of which will be driven by one or multiple p-channel mosfets connected to the ESP32’s LED PWM pin. This gets us 1A of PWM output for brightness control.

Each ESP32 Pin can safely sink 28mA typical. Will limit this to 25mA and install a ~72 Ohm resistor for the purpose of current limiting. May be able to get away with something less. Will warrant experimentation.